FIELD-EFFECT-BASED SEMICONDUCTOR PLATFORM FOR BIO- 
AND CHEMICAL SENSORS

### Michael J. Schöning

Institute of Nano- and Biotechnologies, Aachen University of Applied Sciences, Jülich Campus, Jülich, Germany & Institute of Bio- and Nanosystems 2, Research Centre Jülich, Jülich, Germany

E-mail: m.j.schoening@fz-Juelich.de

The coupling of semiconductor field-effect devices (FED) together with chemical and biological recognition elements, like functional intelligent materials, biomolecules and living cells, represents an attractive platform for the creation of various bio- and chemical sensors, multi-parameter analysis systems and bio-chips.

This paper gives a review on recent developments and current research activities in the field of (bio-)chemically modified FEDs, scaling down from capacitive EIS (electrolyte-insulator-semiconductor) sensors and LAPS (light-addressable potentiometric sensor) to ISFETs (ion-sensitive field-effect transistor) that have been realized in our laboratory. Selected examples of application of ISFETs for the detection of physical parameters in liquids are presented, too.

With the aim of future development of nano-devices for the detection of single biomolecules, the possibility of a simple preparation of different self-aligned nano-structures by using conventional photolithography and pattern-size reduction technique will be experimentally demonstrated.