A NEW AEROSOL DETECTOR FOR HPLC

Neil R. Herbert1, Charles E. Billy2 & Fiona Power3

1Grace Davison Discovery Sciences, Carnforth, Lancashire, UK
discoverysciences.uk@grace.com

2Quant Technologies LLC, Blaine, Minnesota, USA
www.quanttechnologies.com

3Grace Davison Discovery Sciences, Lokeren, Belgium
discoverysciences.be@grace.com

A new, universal HPLC detector is described, the NQAD (Nano Quantity Analyte Detector). It is a new and completely different kind of aerosol-based detector for HPLC which can be used in parallel with UV and MS detection. HPLC detectors used in pharmaceutical analysis are increasingly pushed to their limits for sensitivity and universal detection. The NQAD uses condensation nucleation technology to produce a detector with high sensitivity and excellent linearity over a wide dynamic range.

The patented Water Condensation Particle Counter within the NQAD condenses water vapour onto the dried particles from the nebuliser and heated drift tube and grows them to a size where individual particles can be detected easily using an optical detector. This technology, whilst new to HPLC, has been used for many years in, for instance, the nano--technology industry.

The detector is universal in nature with the proviso that the analyte is less volatile than the mobile phase. It can thus be used for non-volatile and semi-volatile compounds. It is compact, simple to operate and compatible with uHPLC systems.

The theory, detection principles and applications will be briefly discussed. The instrument has a wide application range in the fields of pharmaceuticals, natural products, food, beverage and clinical applications. The NQAD is compatible with all HPLC instruments.