AMOXICILLIN DEGRADATION PRODUCTS IN VARIOUS AQUATIC ENVIRONMENTS

Igal Gozlan1/2,  Adi Mayer1 & Dror Avisar1

1Hydrochemistry Laboratory, Tel Aviv University, Israel
2TAMI (IMI) Ltd., Institute for Research & Development, Haifa, Israel 26111

Gozlan@tami-imi.icl-ip.com

This study examined the chemical behavior of selected antibiotic, amoxicillin (AMX), in variable aquatic environmental conditions in order to determine its degradation products. HPLC–UV-MS/MS and NMR were used to detect and quantify these compounds. These analytical tools were followed up by sample preparation methods such as liquid-liquid extraction, SPE and preparative HPLC. The AMX, which was kept on natural environmental conditions, showed degradation products such as: penicilloic acid, penilloic acid, diketopiperazine amoxicillin, amoxicillin oxide and 3-(4-hydroxyphenyl) pyrazin-2-ol.

Subsequently, several of these degradation products were detected in the aquatic environment (wastewater, effluent and groundwater) at levels of ppb's.