PHOTO-DEGRADATION OF SULFADIMETHOXINE IN WATER BY MEDIUM PRESSURE UV LAMP

Yaal Lester1, Igal Gozlan2,3, Dror Avisar2 & Hadas Mamane1

1School of Mechanical Engineering, Faculty of Engineering, Tel Aviv University, Tel-Aviv, 
69978, Israel
2The Hydro-chemistry Laboratory, Geography and the Environment, Tel-Aviv University, 
Tel Aviv, 69978, Israel
3TAMI (IMI) Ltd., Institute for Research & Development, Israel 26111

Yaal@eng.tau.ac.il;

hadasmg@post.tau.ac.il

The photodegradation rate of Sulfadimethoxine (SMT) in water was studied under polychromatic UV light, in a bench scale apparatus. SMT photolysis was carried out at pH 2.5, 6.5 and 10 to study the impact of acid base properties on degradation of SMT. The highest SMT photolysis fluence based rate was found at pH=2.5 (k=7.22(10-4 cm2/mJ) and the lowest rate at pH=10 (k=4.72(10-4 cm2/mJ), thus reaction rate decreases with increase in pH between pH values of 2.5-10. Results indicated that direct photolysis is not satisfactory for degradation of SMT by polychromatic UV lamp as a fluence of about 7000 mJ/cm2 is needed to break down 99% of SMT at pH 6.5. The photodegradation products of SMT were studied at various pH values. Photodegradation of SMT results in dissimilar relative amounts of intermediates formed at different pH values which may exert a photon demand and impact SMT photodegradation rate.