ANALYSIS OF MOLECULES AND PROTEINS BY ONLINE ELECTROCHEMICAL FLOW CELL / MASS SPECTROMETRY

Vitaly Gutkin, Jenny Gun and Ovadia Lev

The Institute of Chemistry, The Hebrew University of Jerusalem, ISRAEL

During the last years the Laboratory of Environmental Chemistry is developing a novel tool for analysis of the intermediates and by-products of electrochemical reactions by electrochemical flow-cell coupled directly to an on-line mass spectrometer. On-line methods are preferable in electrochemistry over preparative electrolysis followed by ex-situ analysis, since they minimize interferences, contaminations, electrode fouling and oxygen penetration. We have introduced thin radial flow cell equipped with a miniature working electrode. The miniature electrode guarantees minimal uncompensated Ohmic drop within the flow cell, and the very thin layer configuration provides high conversion even for small electrodes at relatively high flow rates. Recently, we have developed a modified version of the EC/ESI-MS instrument for electrochemical preconcentration, desorption and analysis of analytes by EC/ESI-MS. The principle of the analysis is the following: first, a silver layer is electrochemically deposited on the working electrode of a regular EC/ESI-MS. Then, an alkyl thiol functionalized with a desirable ligating group is electrochemically deposited on the silver layer. In a third step, this construction is exposed to a flow stream containing the analyte. The silver - carrying the thiol and the adsorbed analyte is then stripped electrochemically and the dissolved species are carried to the ESI-MS detector. The electrochemical deposition – stripping method, coupled with on-line electrospray ionization mass-spectrometry can be successfully used for determination and identification of various thiols. A modified method allows for the determination of virtually any analyte by its chelation to a functionalized thiol bound to a silver electrodeposit.

Gutkin, V., Gun, J., Lev, O. Electrochemical Deposition – Stripping Analysis of Molecules and Proteins by Online Electrochemical Flow Cell/Mass Spectrometry. Analytical Chemistry, 81 (20), 8396-8404, 2009.

Experimental setup: Analysis of selectively accumulated analytes by deposition of silver, electrochemically accelerated self-assembly of thiolated ligands, selective capture of the target analyte (avidin) and finally anodic electrochemical desorption of the silver ions along with the captured analyte to the ESI-MS.