MEASURING ISOTOPE RATIOS WITHOUT MASS SPECTROMETERS

Richard N. Zare

Department of Chemistry, Stanford University

Stanford, California 94305-5080 USA

zare@stanford.edu

A continuous-flow cavity ring-down spectroscopy (CRDS) system comprising a chromatographic separation technique, a catalytic combustor, and an isotopic 13C/12C optical analyzer is described for the isotopic analysis of a mixture of organic compounds. A demonstration of its potential is made for a geochemically important class of short-chain hydrocarbons. The system proved to be linear over a three-fold injection volume dynamic range with an average precision of 0.95 ‰ and 0.67 ‰ for ethane and propane, respectively. The calibrated accuracy for methane, ethane, and propane is within 3 ‰ of the values determined using isotope ratio mass spectrometry (IRMS), which is the current method of choice (gold standard) for compound-specific isotope analysis. With anticipated improvements, the low cost, portable, and easy-to-use CRDS-based instrumental setup is poised to evolve into a credible challenge to the high-cost and complex IRMS-based technique. Moreover, the approach described is quite general and can be applied to the determination of many other compound-specific isotopic ratios.