SYSTEM OPTIMIZATION OF FLOW-THROUGH WHOLE CELL OPTICAL BIOSENSOR

- Elbaz1, M. Burstin1, E. Eltzov3 and R.S. Marks1,2,3,4

1Department of Biotechnology Engineering, Ben-Gurion University of the Negev, P.O.Box 653, Beer-Sheva 84105, Israel

2National Institute for Biotechnology in the Negev, Ben-Gurion University of theNegev, P.O. Box 653, Beer-Sheva 84105, Israel

3Unit of Environmental Engineering, Faculty of Engineering Science Ben-GurionUniversity of the Negev, P.O. Box 653, Beer Sheva 84105, Israel

4The Ilse Katz Center for Meso and Nanoscale Science and Technology, Ben-GurionUniversity of the Negev, P.O. Box 653, Beer-Sheva 84105, Israel

We demonstrate a system optimization of different parameters of a bioluminescent bacteria based photodetector to detect toxins in a flow through system which can act as an alerting system for pollutants in water sources. The bioluminescent bacteria are immobilized on fiber optic tips, so after exposure to toxicants it can emit light which can then be measured by a photodiode	
 System parameters such as the bacterial immobilization matrix on fibers (2% (w/v) low viscosity sodium alginate solution and 2% LB-agar), flow rate, media type and concentration together with different ethanol concentrations as the model analyte, were tested during continuous 4-hour measurements (4HM). It was observed that the optimal immobilization matrix was sodium alginate in terms of sensitivity of the test. The flow rate was set on 1.5 L/hr while the most sensitive reaction to a positive control flowing was observed in 7.5% (v/v) for all three media that were tested however 2YT medium had shown the highest signal of all.