5975-SMB – A New Supersonic GC-MS with Advanced Capabilities

Aviv Amirav,  Alexander Gordin,  Alexander B. Fialkov,

Tal Alon,  Eli Flaxer

School of Chemistry, Tel Aviv University, Tel Aviv, Israel

A new GC-MS with Supersonic Molecular Beams (SMB) (Supersonic GC-MS) system was designed and optimized at Tel Aviv University and it is now available by Aviv Analytical from Hod Hasharon Israel. It is based on the combination of the SMB technology with the Agilent 5975 GC-MS (or 7000), forming a new and powerful GC-MS system named 5975-SMB. Supersonic GC-MS is based on GC and MS interface with SMB and on the electron ionization of sample compounds in a fly-through ion source. The GC eluting sample compounds are mixed with helium make up gas, expand from a supersonic nozzle into a vacuum chamber, vibrationally cooled, skimmed, and pass a contact-free EI ion source where they are ionized and mass analyzed. 
The 5975-SMB provides the following main benefits.   

A) Improved sample identification through exhibiting enhanced molecular ions and isomer MS effects combined with the usual EI fragments. Isotope abundance analysis software complements library identification through the provision of elemental formulas and confirmation or rejection of library identification.   

B) The range of thermally labile and low volatility samples amenable for analysis is significantly extended thereby bridging the gap between GC-MS and LC-MS. 

C) The detection sensitivity is improved particularly for samples that are hard to detect by standard GC-MS via the enhancement of molecular ions and elimination of vacuum background and ion source peak tailing and degradation. 

D) Effective fast and ultra fast GC-MS is provided via the use of high column flow rate in combination with a unique low thermal mass fast GC inlet. 

Diverse range of applications will be demonstrated including: hydrocarbons, fuels, Biodiesel, geochemical, forensic, explosives, pesticides, environmental, drugs, food and general service GC-MS. The 5975-SMB will be presented from basic chemical physics concepts to advanced hardware and to the establishment of analytical instrument industry in Israel.